UBIFS file system
Adrian Hunter (Адриан Хантер)
Artem Bityutskiy (Битюцкий Артём)

---
Plan
Introduction (Artem)
MTD and UBI (Artem)
UBIFS (Adrian)
[Speaker Notes: First of I define the scope of UBIFS, the area it is designed for, and the area it is not designed for. This is very important because people are often confused about where they can use UBIFS.]

---
UBIFS scope
UBIFS stands for UBI file system (argh...)
UBIFS is designed for raw flash devices
UBIFS is not designed for SSD, MMC, SD, Compact Flash, USB sticks, and so on
  - I call them “FTL devices”
  - They have raw flash inside, but they are block devices
  - They are very different to raw flash devices

---
UBIFS scope

---
UBIFS scope
UBIFS is designed for raw flash devices
E.g. NAND, NOR, OneNAND, etc

---
FTL device vs. Raw flash
Raw flash and block device are completely different

---
FTL devices
FTL stands for “Flash Translation Layer”
FTL devices have raw flash plus a controller
Controller runs FTL firmware
FTL firmware emulates block device
Block I/O interface
(USB mass storage, MMC, etc)
FTL
NAND array

---
FTL devices – cons and pros
One may run trusted traditional software (e.g., ext3)
Standardized
Black box, FTL algorithms are trade secrets
Fast wear-out and death reports
Data corruption reports
Historically designed for FAT FS
Optimized for FAT

---
UBIFS goals
Fix JFFS2 scalability issues
  - Faster mount
  - Fast opening of big files
  - Faster write speed
But preserve cool JFFS2 features
  - On-the-flight compression
  - Tolerance to power cuts
  - Recoverability

---
Plan
Introduction (Artem)
MTD and UBI (Artem)
UBIFS (Adrian)
[Speaker Notes: I'm going to talk about MTD and UBI a little, because UBIFS depends on.]

---
UBI/UBIFS stack
UBIFS
(fs/ubifs)
UBI
(drivers/mtd/ubi)
MTD
(drivers/mtd)
NAND
NOR
OneNAND
etc
Flash hardware
(NAND, NOR, etc)

---
MTD
MTD stands for “Memory Technology Devices”
Provides an abstraction of MTD device
Hides many aspects specific to particular flash
Provides uniform API to access various types of flashes
E.g., MTD supports NAND, NOR, ECC-ed NOR, DataFlash, OneNAND, etc
Provides partitioning capabilities

---
MTD API
In-kernel API (struct mdt_device) and user-space API (/dev/mtd0)
  - Information (device size, min. I/O unit size, etc)
  - Read from and write to eraseblocks
  - Erase an eraseblock
  - Mark an eraseblock as bad
  - Check if an eraseblock is bad
Does not hide bad eraseblocks
Does not do any wear-leveling

---
UBI
Stands for “Unsorted Block Images”
Provides an abstraction of “UBI volume”
Has kernel API (include/mtd/ubi-user.h) and user-space API (/dev/ubi0)
Provides wear-leveling
Hides bad eraseblocks
Allows run-time volume creation, deletion, and re-size
Is somewhat similar to LVM, but for MTD devices

---
UBI/UBIFS stack
UBIFS
(fs/ubifs)
UBI
(drivers/mtd/ubi)
MTD
(drivers/mtd)
NAND
NOR
OneNAND
etc
Flash hardware
(NAND, NOR, etc)

---
UBI volume vs. MTD device

---
Main idea behind UBI
Maps LEBs to PEBs
Any LEB may be mapped to any PEB
Eraseblock headers store mapping information and erase count
LEB
UBI volume
MTD device
PEB
Bad PEB

---
UBI operation example
1. Write data to LEB0
a) Map LEB0 to PEB1
b) Write the data
2. Write data to LEB1
, LEB4
3. Erase LEB1
a) Un-map LEB1 ...
return
b) Erase PEB4 in background
4. Write data to LEB1
LEB0
LEB1
LEB2
LEB3
LEB4
LEB5
UBI volume
MTD device
PEB0
PEB1
PEB2
PEB3
PEB4
PEB5
PEB6

---
UBI bad eraseblock handling
1% of PEBs are reserved for bad eraseblock handling
If a PEB becomes bad, corresponding LEB is re-mapped to a good PEB
I/O errors are handled transparently

---
Write error handling example
1. User writes data to LEB0 ...
a) Select a good PEB to recover the data to ...
PEB4
b) Recover the data by copying it to PEB4
c) Re-map LEB0 to PEB4
d) Write new data again
e) Recovery is done! Return from UBI
f) Erase, torture and check PEB1 in background ...
and mark it as bad
LEB0
UBI volume
Write error!
MTD device
PEB1
PEB4

---
Other
Handle bit-flips by moving data to a different PEB
Configurable wear-leveling threshold
Volume update operation
Volume rename operation
Suitable for MLC NAND
Performs operations in background
Works on NAND, NOR and other flash types
Tolerant to power cuts
Simple and robust design

---
Atomic LEB change
Very important for UBIFS
Suppose LEB0 has to be atomically updated
a) Select a PEB ...
PEB0
b) Write new data to PEB0
c) Re-map LEB0 to PEB0
d) Done! Return from UBI
e) Erase PEB2 in background
LEB0
UBI volume
MTD device
PEB0
PEB2

---
UBI Scalability issue
Unfortunately, UBI scales linearly
UBI reads all eraseblock headers on initialization
Initialization time grows with growing flash size
But it scales considerably better than JFFS2
May be improved
UBI2 may be created, UBIFS would not change
Suitable for 1-16GiB flashes, depending on I/O speed and requirements

---
Plan
Introduction (Artem)
MTD and UBI (Artem)
UBIFS (Adrian)

---
UBIFS relies on UBI
UBIFS does not care about bad eraseblocks and relies on UBI
UBIFS does not care about wear-leveling and relies on UBI
UBIFS exploits the atomic LEB change feature

---
Requirements
Good scalability
High performance
On-the-flight compression
Power-cut tolerance
High reliability
Recoverability
[Speaker Notes: I do not give details on what UBIFS is doing to fulfill the requirements now. But the requirements pretty much defined the UBIFS design. At the end of the presentation, I'll come back to this list of requirements and comment on each of them some more.]

---
File System Index
Index allows to look-up physical address for any piece of FS data
File “foo”
File “bar”
A
B
A
B
C
Index
B
A
A
C
B
UBI volume
MTD device

---
JFFS2 index
JFFS2 does not store the index on flash
On mount JFFS2 fully scans the flash media
Node headers are read to build the index in RAM
JFFS2 node
Data
Header
MTD device

---
UBIFS index
UBIFS index is a B+ tree
Leaf level contains data
Tree fanout is configurable, default is 8
.............................................................................
Leaf level contains FS data
Index

---
UBIFS Index
UBIFS index is stored and maintained on flash
Full flash media scanning is not needed
Only the journal is scanned in case of power cut
Journal is small, has fixed and configurable size
Thus, UBIS mounts fast
................................................................
Journal
UBIFS

---
Out-of-place updates
Flash technology and power-cut-tolerance require out-of-place updates
Change “foo” (overwrite A, B, C)
A
B
C
File “/foo”:
1. Write “A” to a free space
2. Old “A” becomes obsolete
3. Write “B” to free space
4. Old “B” becomes obsolete
5. Write “C” to free space
6. Old “C” becomes obsolete
Index
Data
Obsolete
Obsolete
Obsolete
But how about the index?
A
B
C
A
A
B
B
I
C
C
UBIFS
I
.........................................................................................
A
B
C
[Speaker Notes: Show the idea of out-of-place updates. Tell that this is fine for JFFS2, but UBIFS has the index. Prepare ground to introduce wandering trees.]

---
Wandering trees

---
Wandering trees
A
A
A
1. Write data node “D”
2. Old “D” becomes obsolete
3. Write indexing node “C”
4. Old “C” becomes obsolete
5. Write indexing node “B”
6. Old “B” becomes obsolete
B
B
B
7. Write indexing node “A”
6. Old “A” becomes obsolete
C
C
C
D
D
D
How to find the root of the tree?
D
A
A
B
B
A
D
D
C
C
C
B
UBIFS
[Speaker Notes: Explain wandering tree mechanisms. At the end ask logical question – how to find the root of the tree on mount?]

---
Master node
Stored at the master area (LEBs 1 and 2)
Points to the root index node
2 copies of master node exist for recoverability
Master area may be quickly found on mount
Valid master node is found by scanning master area
1. Suppose “R” is changed
6. LEBs 1 and 2 become full
2. Then “M” is updated
7. LEB 1 is erased
3. Old “M” becomes obsolete
8. “M” is written
4. The same is done to the 2nd copy
9. The same for the 2nd copy
5. and so on ...
LEB 0
M
M
M
M
M
M
M
M
M
M
M
M
R
R
R
R
R
R
UBIFS
Master area (LEBs 1 and 2)
Root index node
R
................................................................

---
Superblock
Situated at LEB0
Read-only for UBIFS
May be changed by user-space tools
Stores configuration information like indexing tree fanout, default compression type (zlib or LZO), etc
Superblock is read on mount
Superblock
Master area
UBIFS
LEB0
LEB1
LEB2

---
Journal
All FS changes go to the journal
Indexing information is changed in RAM, but not on the flash
Journal greatly increases FS write performance
When mounting, journal is scanned and re-played
Journal is roughly like a small JFFS2 inside UBIFS
Journal size is configurable and is stored in superblock
[Speaker Notes: It would be extremely inefficient to change whole path up to the root of the indexing tree on every FS change. UBIFS journal allows us to avoid doing this very often.]

---
TNC
Stands for Tree Node Cache
Caches indexing nodes
Is also a B+-tree, but in RAM
Speeds up indexing tree lookup
May be shrunk in case of memory pressure

---
Journal and TNC
Suppose “A”, “B”, ... “H” have to be changed
1. Change leaf node “A”
Tree Node Cache
(in RAM)
2. Look up the index and populate TNC
I1
3. Write “A” to the journal
... and amend TNC
4. Similarly for “B” and “C”
I2
I3
5. And so on for “D”, “E”, “F”, “G”, and “H”
6. Journal is full - commit
I4
I5
I6
I7
Excuse me, but the journal is still full
I1
Indexing tree
(on Flash)
I2
I3
I4
I5
I6
I7
A
A
B
B
C
C
D
D
E
E
F
F
G
G
H
H
A
B
C
D
E
F
G
H
I1
I1
I2
I2
I3
I3
I4
I4
I4
I4
I6
I6
I7
I7
A
A
B
B
C
C
D
D
E
E
F
F
G
H
I1
I2
I3
I4
I4
I6
I7
Journal LEBs

---
Journal is also wandering
After the commit we pick different LEBs for the journal
Do not move data out of the journal
Instead, we move the journal
Journal changes the position all the time

---
More about the Journal
Journal has multiple heads
  - This improves performance
Journal does not have to be continuous
  - Journal LEBs may have random addresses
  - LEBs do not have to be empty to be used for journal
  - This makes journal very flexible and efficient

---
Garbage collection
At some point UBIFS runs out of free space
Garbage Collector (GC) is responsible to turn dirty space to free space
One empty LEB is always reserved for GC
Obsolete data (Dirty space)
Reserved for GC
Valid FS data
Valid indexing data

---
How GC works
GC copies valid data to the journal (GC head)
TNC
1. Pick a dirty LEB ...
LEB1
2. Copy valid data to LEB6
3. LEB1 may now be erased
4. Pick another dirty LEB ...
LEB7
5. Copy valid data to LEB 6
6. LEB 7 now may be erased
I1
I2
I3
I4
8. LEB 1 is reserved for GC, LEB7 is available
9. How about the index?
10. Indexing nodes are just marked as dirty in TNC
Dirty
11. But what if there is no free space for commit?
I1
I2
I4
I3
LEB0
LEB1
LEB2
LEB3
LEB4
LEB5
LEB6
LEB7

---
Commit
Commit operation is always guaranteed to succeed
For the index UBIFS reserves 3x as much space
In-the-gaps commit method is used
Atomic LEB change UBI feature is used
Index
Reserved

---
LEB properties
UBIFS stores per LEB-information of flash
  - LEB type (indexing or data)
  - Amount of free and dirty space
Overall space accounting information is maintained on the media
  - Total amount of free space
  - Total amount of dirty space
  - Etc
Used e.g., when
  - A free LEB should be found for new data
  - A dirty LEB should be found for GC

---
LPT
Stands for LEB Properties Tree
Is a B+-tree
Has fixed size
Is much smaller than the main indexing tree
Managed similarly to the main indexing tree

---
Requirements
Good scalability
  - Data structures are trees
  - Only journal has to be replayed
High performance
  - Write-back
  - Background commit
  - Read/write is allowed during commit
  - Multi-head journal minimizes amount of GC
  - TNC makes look-ups fast
  - LPT caches make LEB searches fast

---
Requirements
On-the-flight compression
Power-cut tolerance
  - All updates are out-of-place
  - Was extensively tested
High reliability
  - All data is protected by CRC32 checksum
  - Checksum may be disabled for data
Recoverability
  - All nodes have a header which fully describes the node
  - The index may be fully re-constructed from the headers